## Slide 1: A Maintenance Program for a bus fleet
Lessons from a Potential CDM Project in India
Kaushik Deb, TERI

## Slide 2: Structure of the presentation
The policy context
CDM and transport: Synergies
Key barriers
The Project
  Need for an effective maintenance
  Inspection Systems: CDM project
  Emission savings
  Cost estimates
Lessons

## Slide 3: Urban transport in India
Large urban population
  Over 1/3 in 2001
High vehicle density in urban areas
  33% concentrated in cities with 10% population
  82% are personal vehicles
Inadequate public transport
  Effective public transport in only 10 cities
  Rail in only 3 cities
No urban transport policy
Diffused institutional arrangements
Implications for economic sustainability
  Cities are vertices of continued growth

## Slide 4: Trends in vehicle population

## Slide 5: Vehicle Ownership
Per capita
income (US $)
Cities
Vehicles Per
1000 Persons
London (1990)
Paris (1990)
Tokyo (1990)
$22,000
$34,000
$37,000
356
383
266
Delhi (1998)
$850
200
Shanghai (2000)
$4,000
69
Notes: As you can see, the members of the Business Environmental Leadership Council are large companies which represent most major sectors of the economy
The diversity of the companies means we have a diversity of activities to reduce greenhouse gas emissions

## Slide 6: Urban travel demand projections
DISHA 2047
Year 2019
5% GDP growth
Sundar & Deb (2000)
7% GDP growth
MoST (1999)

## Slide 7: Vehicular Growth
Notes: India has witnessed a rapid increase in its vehicle population over the last four decades. From a mere 3 million vehicles in the 1960s, the number has gone up to over 35 million by 2000. This growth is expected to continue in the coming years also. Large cities, particularly the metropolitan cities, face a higher concentration of motor vehicles than the smaller towns.
T E R I. 2003
Transportation economics and environmental issues that influence product strategy
New Delhi: The Energy and Resources Institute. 208 pp.

## Slide 8: Policy response in India
Largely technology based response
  Vehicle emissions
  Fuel quality
  Mandating alternative fuels
Inadequate attention to demand management
  NMT discriminated against in resource
  Land use development haphazard, not in sync with transport planning
  Public transport not encouraged, personal vehicles have become more accessible

## Slide 9: Emission norms
New vehicles
1991: First mass emission norms (CO & HC)
1995: Catalytic converters for cars in 4 metros
1996: Further tightening of norms (CO, HC & NOx)
2000: Bharat Stage I (~EUROI)
2001: Bharat Stage II in Delhi (~EURO II)
Sustained progress!!!
In use vehicles
1989: Idle emission regulation
2004: Some tightening
Piece meal efforts
No Statutory Maintenance & Fuel Efficiency Requirements !!!

## Slide 10: Government’s Auto Fuel Policy
April 2010
11 major cities
April 2005
11major cities
April 2003
7 cities other than metros
Entire country
Entire country
All other new vehicles
Entire country
(preferably from April 2008)
Entire country
2 & 3 wheelers
Bharat Stage IV
Bharat Stage III
April 2010
Bharat Stage II April 2005
Category
Notes: Dates of implementation need fine-tuning. Need to study each state’s level of implementation to decide how it can be accelerated.
Export market and the level of stringency in emission norms in these regions.

## Slide 11: Need for an effective system for in use vehicles
Norms very lax
  No consistent improvement
Limited coverage
  Only idle tests for CO (petrol)
  Free acceleration tests for smoke (diesel)
Limited regulatory ability
  Equipment not calibrated
  No auditing/ training
Weak maintenance system

## Slide 12: Synergizing Objectives
Global
  Significant potential for GHG mitigation in transport in India
National
  Positive impacts on local air quality, health & safety
  High priority for urban centres
  Revenue from carbon credits

## Slide 13: GHG emissions from transport
OECD & IEA 2001
1999

## Slide 14: Fuel consumption & GHG emissions in Urban India
Notes: Trip length increases by 37.5% by 2025
At least 60% of the urban travel demand should be catered to by public transport compared to the current 54%. This also implies an increase in the modal share of such intermediate modes of public transport as taxis and passenger three-wheelers from the current 20% to about 23%.
The strategies outlined above should achieve a 25% reduction in emissions per vehicle by 2025 and 50% by 2050 through improved vehicle technology and fuel quality. Also, the following technology mix is being considered to cut down emissions.
The share of ordinary diesel-powered cars in the total fleet of personal vehicles to be maintained at the present level of 15% — the present trend, if it continues unchecked will increase this figure to 35% by 2050.
The share of ordinary diesel-powered IPT (intermediate public transport) in the total fleet of personal vehicles to be maintained at the present level of 25% — the present trend, if it continues unchecked will increase this figure to 50% by 2050.
The share of vehicles powered by CNG (compressed natural gas), ULSD (Ultra Low Sulphur Diesel), and cleaner gasoline, to rise to about 25% of the total personal and IPT vehicle fleet by 2050. This will be a substantial jump increase; the present trend will lead to only a 10% share by 2050.
The share of zero-emission vehicles, such as those powered by fuel cells or solar power, should rise to about 25% of the total personal and IPT vehicle fleet by 2050—again, the present trend will take it to only about 5% by 2050.
Finally, the entire urban bus fleet will run on CNG or ULSD.

## Slide 15: Air quality is a concern

## Slide 16: Transport contributes 3-22% of PM emissions

## Slide 17: Financial performance of public transport operators in India
Costs per
km
Revenue
per km
400
600
800
1000
1200
1400
1600
1800
1990
1992
1994
1996
1998
Rupees

## Slide 18: Barriers
Baselines
  data availability
  uncertain sectoral forecasts
Leakages
  Fuel efficiency Vs VOCs
Monitoring and verification costs
  dispersed and large number of mobile sources
Additionality
  Mandated use of alternative fuels
  Comprehensive I&C regime proposed

## Slide 19: Project description
Existing maintenance regime inadequate and primitive
  Even minor improvements would have large benefits
GHG savings from
  Better maintenance
  Result: Improved energy efficiency. Hence
    GHG savings, Local emissions benefits
Impact: Range estimate of GHG reduction
  5% improvement in fuel efficiency in US (Das et al 2001)
  5.5% improvement in Jakarta (Cornie)
  12.6% improvement in fuel efficiency (USEPA IM240 Program)
  10-20% improvement in fuel efficiency in India (Das et al)

## Slide 20: Project structure
Project proponent: Thane Municipal Transport Undertaking
  Statutory public bus company
  Owned by Thane Municipal Corporation
Mandate: Provide transport services to Thane
Activities
  Bus operation
  Depots and terminals
  Bus maintenance

## Slide 21: Bus fleet covered in the program

## Slide 22: Maintenance checklist
Visual safety tests
  Steering
  Chassis
  Fuel tank & piping
  Engine mountings
  Battery terminals etc
  Seatbelts
  Lighting
  Oil leakages
  Leaf springs…
Automated safety tests
  Headlamp beam
  Brakes
  Sideslip
Emissions
  Volumetric concentration for gasoline
  Opacity for diesel

## Slide 23: Design issues
Project boundary
  Government owned bus company. Reduces
    institutional complexity
    data requirements, thus project development costs
Operational lifetime
  Life of equipment = 15 years
Crediting period: 10 years
  Reduced uncertainty
Monitoring & verification
  Fuel consumption already monitored daily
  Hence, no expense on monitoring

## Slide 24: Emission savings: Methodology
GHG emissions
Vehicle kms
Baseline projections based on
  Existing travel trends
  Expected changes in emission factors, fuel efficiencies
    Increasingly stringent norms
    Improved technology
Sustained improvements in efficiency:5%
Reference years: 2005 & 2015

## Slide 25: GHG savings
Baseline
Reduction scenario

## Slide 26: Project costs
Net present value of project
  — US$ 0.13 million
Project cost
  US$ 0.54 million
Cost of CO2
  ~ US$ 8.5
Substantial local benefits

## Slide 27: Transport CDM projects: Lessons
Baselines
  Carry out pilot tests to estimate fuel efficiency gains
Leakages
  Captive fleet with fixed mobility
  Independent of VOCs, exogenously determined demand
Monitoring and verification costs
  Data already monitored independently
  Preexisting statutory auditing: CAG
Additionality
  Comprehensive I&C regime proposed in India
  But no maintenance guidelines, requirements

## Slide 28: Structure of a CDM project
The Executive Board
Baselines
  Additionality
  Leakages
Monitoring & verification
CER market
Price of CERs
  Total CERs
  Cost of project
Cost issues
  Equity/Debt Vs revenue streams
  CER revenues only as revenue streams!!!

## Slide 29: Structure the project well!!!